## Slide 1: AMPQ based pipeline communication
Wouter Klijn

## Slide 2: Content
Problem description
Proof of concept
Performance analysis
Analysis
Bus infrastructure
Stateless Micro Service Based design
Reusable components

## Slide 3: Problem description
A list of communication problems in the LOFAR pipeline system
  Hanging node jobs
  Partial communication
  Exceptions
Root cause:
  SSH based starting of Jobs
  Socket based communication with homebrewed protocol
  Root cause? Dependency on software close in stead of layer close connection (Jan David knows best)

## Slide 4: Proof of concept
Quick and dirty implementation of a Master Slave based communication protocol.
Main goals:
  Is it even possible in the pipeline framework.
  Performance
  Hands on experience with QPID
Minimal changes in the pipeline framework
Based on statically named queues
Aim for fault tolerant behaviour and self cleaning

## Slide 5: Proof of concept

## Slide 6: Proof of concept
2000 lines of code, 500 lines of testing code
The interfacing with pipeline is ugly:
  Node level needs 20 lines of ugly code to get the information needed
  Top-level interface needs a fragile threaded interface, the existing interrupt handling (ctrl-c ctrl-z) does not play nice with new framework
  Initially performance issues

## Slide 7: Performance analysis
Running two pipelines. 80 * 2 node jobs. 3 steps
Runtime increases, peak performance decreases
Problem worsens in time
Chart: Number of established and Time waiting connection on the QPID port

## Slide 8: Performance analysis
Manually close on all created connection
Running two pipelines. 80 * 2 node jobs. 8 steps
Lesson: DO NOT TRUST PYTHON MEMORY MANAGEMENT
Chart: Number of established and Time waiting connection on the QPID port

## Slide 9: analysis
The Master node structure is performant.
  There is a limit regarding the number of open connection (OS dependent, default should NOT be changed)
  The maximum number can be increased on the QPID side, not expected under currently expected load. Nice to have when needed.
The current integration in the framework should be clean: Will lead to changes on the pipeline interface
Mixing of pipeline and qpid functionality: Aim for separation of responsibilities.
Self cleaning with queues is hard

## Slide 10: Bus based design
Using QPID functionality it is possible to create a star base bus structure.
What is boils down to is that with some handwaving and a magic dance beforehand (implemented by Jan Rinze) you have a generic bus structure.
Eg. Sender connects to busname/id
  If there is NO listener the msg will end up in a dead letter queue. This can trigger behaviour
  Any listener can ‘register’ to an id

## Slide 11: Stateless Micro Service Based design
Stateless, all work is done based on msg. No information is kept between events.
  Errors do not interfere with other work, only a single job might fail.
  Fail over, if it breaks down, restart and continue
  Horizontal scaling
Micro service, do one thing well and nothing more
  Separation of responsibilities
  Reuse
  Reduction of problem space

## Slide 12: Stateless Micro Service Based design

## Slide 13: Reusable components
CQDaemon: abstract interface.
  Pols command queue
  Single command: Quit
HCQDaemon: Implements CQDaemon
  Adds start_job command
Log topic handler:
  Master: Receives loglines, puts them on the logger
  Slave: Python loghandler, receives normal loglines, posts them on a qpid topic
Results Handler: Receives result on queue
  Insert into internal storage
  Can be started as a thread

## Slide 14: TODO
Subprocess starter
Deadletter queue handling
Clean interfacing with pipeline framework
Configuration
Validation bus config